## Slide 1
Office of Science
SciDAC-II
Compass
Modeling of 10 GeV-1 TeV Laser-Plasma Accelerators using Lorentz Boosted Frame Simulations
J.-L. Vay, C. Geddes, E. Esarey, W. Leemans, C. Schroeder (LBNL, CA, USA), D Grote (LLNL, CA, USA), E. Cormier-Michel (Tech-X, CO, USA)
Hyperbolic rotation from Lorentz Transformation converts laser spatial oscillations into time beating,
==> enabling high levels of digital filtering without altering the physics.
Lab frame
Wake frame
Time
Time
Laser field
Laser field
Like a speedboat leaving a wake that a surfer can ride, a laser pulse in a laser-plasma wakefield accelerator creates a wake in the plasma that an electron beam “surfs” to high energy.
Energy
Emittance
Xr.m.s.
Warp – 2-1/2D – 10 GeV stage – gboost=10
Cole-Karkkainen
EM solver with tunable numerical dispersion
J.-L. Vay, et al., J. Comput. Phys. 230 (2011)
“Strided” digital filtering
Special time step
Instability level
Time step
Yee
Exact
Speedup Limitations have been Overcome
J.-L. Vay, et al., PoP Lett. 18 030701 (2011)
J.-L. Vay, C. Geddes, E. Esarey, W. Leemans, C. Schroeder, D. Grote, E. Cormier-Michel PoP 18 123103 (2011)
Laser-Plasma Acceleration (LPA)
Lorentz Boosted Frame Method
In the laboratory frame, millions of time steps are necessary to simulate from first principles a l=0.8 mm laser through a 0.8 m plasma column. In a Lorentz boosted frame, the plasma column is contracted by g, the laser expands by ~2g, and the number of time steps is divided by 2g2.
J.-L. Vay, Phys. Rev. Lett. 98, 130405 (2007)
Full Scale Simulations of 0.1 GeV – 1 TeV Stages
L=0.8 m
l=0.8 m
0.8 m/0.8 m=1,000,000.
Lab frame
compaction
X20,000.
l’=0.16 mm
8 mm/0.16 mm=50.
Boosted frame  = 100
Hendrik Lorentz
L’=8 mm
A strong instability has been observed in boosted frame PIC simulations for large g.
2D
3D
Novel numerical techiques (tunable elecromagnetic solver, “strided” digital filter), and a time step at which the instability growth is greatly reduced, enable efficient mitigation of the instability.
Warp 2-1/2D 10 GeV LPA (ne=1017cc, =130)
Longitudinal electric field
laser
plasma
In the boosted frame, the Rayleigh length of the laser is contracted by g, while its transverse size increases as g2, preventing the initialization of the entire laser at once.
A novel method launching the laser from a moving planar antenna was developed.
The boosted frame method has been benchmarked carefully on a 0.1 GeV LPA stage. Agreement has been obtained at the % level between simulations at various g.
Boosted frame method enables modeling of fully depleted 10 GeV-1 TeV stages.
J.-L. Vay, et al, PoP 18 123103 (2011)